## Slide 1: Introduction to TCP/IP punkis@attrition.org

## Slide 2: Intro to TCP/IP What this lecture is
This lecture will give a general low-level overview of TCP/IP
This lecture is geared toward novices
If you want a high level overview of TCP/IP go buy TCP/IP Illustrated

## Slide 3: Intro to TCP/IP History - The Beginning
1969 - Advanced Research Project Agency (ARPA) funds research and development of an experimental packet-switching network (ARPANET)
ARPA’s goal was to study techniques for providing robust, vendor independent data communications

## Slide 4: Intro to TCP/IP History
ARPANET was so successful that many organizations attached to it began to use it on a daily basis
1975 - ARPANET converted from an experimental network to an operational network when the Defense Communications Agency (DCA) took control of it

## Slide 5: Intro to TCP/IP History - 1983
TCP/IP protocols developed as Military Standards. All hosts on the network were required to convert to the new protocols
DARPA funded the implementation of TCP/IP in Berkley (BSD) Unix
The term internet came into common use

## Slide 6: Intro to TCP/IP History
1983 - ARPANET is split into MILNET and a new smaller ARPANET
1985 - The National Science Foundation (NSF) creates NSFNet and connects it to the internet
1987 - NSF creates a new faster backbone and a three-tiered topology that includes backbone, regional networks, and local networks

## Slide 7: Intro to TCP/IP History
1990 - ARPANET passes out of existence.
1995 - NSFNet ceases its role as primary backbone for the internet

## Slide 8: Intro to TCP/IP History - In a Nutshell
What has come to be known as the internet was originally an experiment used primarily by researchers and developers
The internet has grown much larger than it was originally designed for
The original networks and agencies involved in the creation of the internet no longer play an essential role

## Slide 9: Intro to TCP/IP Myths
Contrary to what he may think, Al Gore did NOT invent the internet.
Mr. Gore was 21 years old when ARPA funded research and development of ARPANET

## Slide 10: TCP/IP Defined
Transmission Control Protocol/Internet Protocol:
The suite of networking protocols that have been used to construct the global Internet. Also referred to as the DoD or ARPANET protocol suite because their early development was funded by the Advanced Research Projects Agency (ARPA) of the US Department of Defense (DoD).

## Slide 11: TCP/IP In a Nutshell:
The series of protocols that allow computers to communicate with one another regardless of Operating System or vendor

## Slide 12: The 4 layers of TCP/IP
Application
Transport
Network
Link
Telnet, FTP, mail, etc
TCP, UDP
IP, ICMP, IGMP
Device Driver and Interface Card

## Slide 13: The 4 layers of TCP/IP
Link layer (Data link layer)
This layer includes the device driver in the OS and the corresponding network interface card in the computer. Handles the hardware details of physically interfacing with the network.

## Slide 14: The 4 layers of TCP/IP
Network Layer (Internet Layer)
Handles the movement and routing of packets around the network

## Slide 15: The 4 layers of TCP/IP
Transport Layer
Provides a flow of data between two hosts for the Application Layer above. Two different Transport protocols are used at this level:
TCP: Reliable. Breaks data passed from the Application Layer above into chunks for the Network Layer below, acknowledging received packets setting timeouts, etc.
UDP: Unreliable. Sends packets of data (Datagrams) from one host to another with no guarantee packets will reach their destination.

## Slide 16: The 4 layers of TCP/IP
Application Layer
This layer handles the details of the particular application being used. Some standard TCP/IP applications include:
  Telnet
  FTP
  SMTP
  SNMP

## Slide 17: The 4 layers of TCP/IP
Encapsulation
When an an application sends data using TCP, it is sent through each layer in the protocol stack.
  Each layer adds information to the data by adding a header and sometimes a footer.
  The data is then sent as a stream of bits across the network

## Slide 18: The 4 layers of TCP/IP
IP Layer
Link Layer
Application Layer
TCP Layer
User Data
Application
Header
User Data
TCP
Header
Application Data
TCP
Header
Application Data
IP
Header
Application Data
TCP
Header
IP
Header
Ethernet
Header
Ethernet
Trailer
TCP Segment
IP Datagram
Ethernet Frame
46 to 1500 bytes
Ethernet
Encapsulation

## Slide 19: The 4 layers of TCP/IP
Demultiplexing
  When an ethernet frame is received by a host it starts its way back up the protocol stack
  Each layer looks at its respective header and decides what to do with the data before passing it up to the next layer

## Slide 20: TCP/IP Networking Protocols

## Slide 21: Internet Protocol IP - Features
The dominant network layer protocol used by the TCP/IP suite of protocols
IP defines the rules for packaging network traffic into IP datagrams and also defines the rules for moving these datagrams across a network
IP is also responsible for fragmenting data wherever necessary and to properly reassemble the datagrams at the other end

## Slide 22: Internet Protocol

## Slide 23: Internet Protocol IP Datagram Fields
• Version: Indicates which version of IP is being used (typically 4)
• Header Length: Indicates how many 4-byte words are in the header
• Type of Service (TOS): Indicates the level of service the IP datagram should be assigned
• Datagram Length: The length of the entire datagram including the header (max size 65,535 bytes)
• Datagram Identification: Uniquely identifies each datagram sent by a host

## Slide 24: Internet Protocol IP Datagram Fields
• Flags: The first of three flags are unused. The Don’t Fragment (DF) and More Fragment (MF) flags control the way a datagram is fragmented
• Fragment Offset: Indicates how many units from the start of the original datagram the current datagram is
• Time to Live (TTL): Indicates how many routers a datagram may traverse before being dropped (max TTL is 255)
• Protocol: Identifies which protocol handed the IP to data
• Header Checksum: A check on the IP header only to ensure the header is not corrupted

## Slide 25: Internet Protocol IP Datagram Fields
• Source/Destination IP Addresses: 32 bit IP addresses of originating host and destination host
• Options: Currently defined options are security and handling restrictions, record route, timestamp, loose source routing, and strict source routing. These options are rarely used
• Data

## Slide 26: Internet Protocol Packet Analysis
IP Header
Version: 4
Header Length: 20 bytes
Service Type: 0x00
Datagram Length: 40 bytes
Identification: 0x5850
Flags: MF=off, DF=on
Fragment Offset: 0
TTL: 32
Encapsulated Protocol: TCP
Header Checksum: 0x9658
Source IP Address: 172.16.10.2 (broken)
Destination IP Address: 172.16.10.5 (testbed)

## Slide 27: Traceroute
There is no guarantee that two connective IP datagrams from the same source to the same destination will take the same route but they usually do
Traceroute is a tool that help to trace the flow of IP datagrams from one host to another

## Slide 28: Traceroute - How it works
Sends an IP datagram with a TTL of 1 to the destination host
The first router to handle the datagram decrements the TTL to 0, throws away the datagram, and sends an ICMP time exceeded back to the host
Traceroute then sends another datagram with a TTL of 2 and we find the IP address of the second router
This continues until the datagram reaches the host

## Slide 29: Traceroute
Sample traceroute output:
  # traceroute victim.com
  traceroute to victim (172.16.1.10), 30 hops max, 40 byte packets
  1 satan (172.16.1.66) 20ms 10ms 10ms
  2 victim (172.16.1.10) 120ms 120ms 120ms
For each TTL 3 datagrams are sent. These values are recorded in the output.

## Slide 30: Transmission Control Protocol TCP - Features
TCP is a transport layer protocol
Provides a way to connect hosts across an network reliably
Provides a ‘virtual circuit’ between two hosts
Communicating hosts are required to acknowledge receipt of network traffic

## Slide 31: Transmission Control Protocol TCP - Features
TCP packages its data into segments which contain both data and session control information
Since segments traversing a network may arrive out of order TCP provides proper reassembly of these segments
Sequence numbers are used to properly reassemble segments

## Slide 32: Sequence Numbers Packet Analysis
Packet 49
TCP: port ftp-data -> 26410 seq=1326731397 ack=1518678629
DATA: 1460 bytes
---------------------------------------------------------------------------
Packet 50
TCP: port ftp-data -> 26410 seq=1326732857 ack=1518678629
DATA: 1460 bytes
---------------------------------------------------------------------------
Packet 51
TCP: port ftp-data -> 26410 seq=1326734317 ack=1518678629
DATA: 1460 bytes
---------------------------------------------------------------------------
Packet 52
TCP: port ftp-data -> 26410 seq=1326735777 ack=1518678629
DATA: 1460 bytes
ftp transfer tcpdump output

## Slide 33: Transmission Control Protocol TCP - Features
Maximizes performance of a connection by ensuring TCP segments are neither too large or too small

## Slide 34: Transmission Control Protocol TCP - In a Nutshell
Virtual circuits - TCP connections behave like a live two-way connection
Reliable connections - TCP segments are guaranteed to reach their destination, if they are not the user is notified
Performance optimization - TCP can modify transmission variables depending on network conditions

## Slide 35: Transmission Control Protocol

## Slide 36: Transmission Control Protocol TCP Header Fields
• Source Port/Destination Port: 16-bit port number or originating host and destination host
• Sequence Number: 4-byte number assigned by TCP starting with an randomly chosen number. This number is used to determine how many bytes have been transmitted across the network
• Acknowledgement Number: Acknowledges the last segment sent by the host
• Header Length: Measures the header length in 4-byte words

## Slide 37: Transmission Control Protocol TCP Header Fields
• Flags: used when negotiating and managing a connection:
URG: Indicates segment being sent is urgent
ACK: Indicates ack number in segment header is valid
PSH: Pass the data to the application as soon as possible
RST: Resets the connection
SYN: Synchronize sequence numbers to initiate a connection
FIN: The sender is finished sending data
• 16-Bit Window Size: The number of bytes the receiving host is willing to accept

## Slide 38: Transmission Control Protocol TCP Header Fields
• 16-Bit TCP Checksum: A checksum of the TCP Header and data
• 16-Bit Urgent Pointer: used only if the URG flag is set
• Options: The most commonly used option is the Maximum Segment Size (MSS) option. Determines the maximum sized segment the sender is willing to receive
• Data: This portion of the TCP segment is optional. When connections are being established or terminated no data is sent

## Slide 39: Transmission Control Protocol Packet Analysis
TCP Header
Source Port: 22 (ssh)
Destination Port: 1714 (<unknown>)
Sequence Number: 1937534412
Acknowledgement Number: 0104479939
Header Length: 20 bytes (data=0)
Flags: URG=off, ACK=on, PSH=off
RST=off, SYN=off, FIN=off
Window Advertisement: 32736 bytes
Checksum: 0xD102
Urgent Pointer: 0

## Slide 40: TCP - Establishing a Connection Three Way Handshake
1: Send SYN ISN=x
2: Send SYN ISN=y, ACK x+1
3: Send ACK ISN y+1
Client
Server
SYN
ACK
SYN / ACK
4: Full connection established

## Slide 41: TCP Three Way Handshake Packet Analysis - Part 1
---------------------------------------------------------------------------
Packet 1
TIME: 19:50:32.912582 (0.040960)
LINK: 00:40:05:E3:09:D0 -> 00:00:C5:38:0D:27 type=IP
IP: strife -> testbed hlen=20 TOS=00 dgramlen=44 id=2864
MF/DF=0/0 frag=0 TTL=64 proto=TCP cksum=E641
TCP: port 24616 -> ftp seq=2735221453 ack=0000000000
hlen=24 (data=0) UAPRSF=000010 wnd=512 cksum=FBEC urg=0
DATA: <No data>
---------------------------------------------------------------------------
  The requesting client sends a SYN (synchronize) segment specifying the port number of the server it wishes to connect to and the client’s ISN (Initial Sequence Number).

## Slide 42: TCP Three Way Handshake Packet Analysis - Part 2
---------------------------------------------------------------------------
Packet 2
TIME: 19:50:32.912792 (0.000210)
LINK: 00:00:C5:38:0D:27 -> 00:40:05:E3:09:D0 type=IP
IP: testbed -> strife hlen=20 TOS=00 dgramlen=44 id=5FF4
MF/DF=0/1 frag=0 TTL=64 proto=TCP cksum=6EB1
TCP: port ftp -> 24616 seq=2809565737 ack=2735221454
hlen=24 (data=0) UAPRSF=010010 wnd=17520 cksum=7FCB urg=0
DATA: <No data>
---------------------------------------------------------------------------
  The server responds with a SYN segment including the servers own ISN. An ACK (acknowledge) is also sent with the clients ISN plus one.

## Slide 43: TCP Three Way Handshake Packet Analysis - Part 3
---------------------------------------------------------------------------
Packet 3
TIME: 19:50:32.913768 (0.000976)
LINK: 00:40:05:E3:09:D0 -> 00:00:C5:38:0D:27 type=IP
IP: strife -> testbed hlen=20 TOS=00 dgramlen=40 id=2865
MF/DF=0/1 frag=0 TTL=64 proto=TCP cksum=A644
TCP: port 24616 -> ftp seq=2735221454 ack=2809565738
hlen=20 (data=0) UAPRSF=010000 wnd=32120 cksum=5E80 urg=0
DATA: <No data>
---------------------------------------------------------------------------
The client acknowledges the servers SYN and sends an ACK segment with the Servers ISN plus one.

## Slide 44: User Datagram Protocol UDP - Features
UDP is a transport layer protocol
Does not use the benefit of error detection, error correction, handshaking, or verification of delivery like TCP
Provides a connectionless delivery system between two hosts
UDP has low overhead

## Slide 45: User Datagram Protocol

## Slide 46: User Datagram Protocol UDP Datagram Format
• Source Port Number: 16-bit port number of originating host. Uses ephemeral ports (greater than 1024)
• Destination Port Number: 16-bit port number of destination host. Uses well-known port numbers
• 16-Bit UDP Length: Indicates the length of the length of entire UDP datagram, including header
• 16-Bit UDP Checksum: A checksum of the entire UDP datagram

## Slide 47: UDP Packet Analysis
UDP Header
Source Port: 2167 (<unknown>)
Destination Port: 53 (domain)
Datagram Length: 37 bytes (Header=8, Data=29)
Checksum: 0xD5B0

## Slide 48: Intro to TCP/IP References
Books
• TCP/IP Illustrated Volume 1
W. Richard Stevens
Addison-Wesley
1994
ISBN:0-201-63346-9
• TCP/IP Network Administration - 2nd Edition
Craig Hunt
O’Reilly & Associates
1998
ISBN: 1-56592-322-7

## Slide 49: Intro to TCP/IP References
WWW
• TCP/IP FAQ Frequently Asked Questions (1999-07) Part 1 of 2
http://www.cis.ohio-state.edu/hypertext/faq/usenet/internet/tcp-ip/tcp-ip-faq/part1/faq.html
• TCP/IP FAQ Frequently Asked Questions (1999-07) Part 1 of 2
http://www.cis.ohio-state.edu/hypertext/faq/usenet/internet/tcp-ip/tcp-ip-faq/part1/faq.html

## Slide 50: Intro to TCP/IP References
Tools
• tcpshow
Tcpshow reads a tcpdump(1) savefile and provides a reason-
ably complete decode of Ethernet, ARP, RARP, IP, ICMP, UDP
and TCP headers, in packets that match the boolean expres-
sion. The data belonging to these packets is displayed in
ASCII.
ftp://ftp.freebsd.org/pub/FreeBSD/packages/net/tcpshow-1.74.tgz
• tcpdump
Tcpdump prints out the headers of packets on a network
interface that match the boolean expression.
ftp://ftp.ee.lbl.gov/tcpdump.tar.Z